## Slide 1: CPE202/CSC201 Microprocessor Programming Tutorial #2
Dr. Sundaram Suresh
N4-02b-67, School of Computer Engineering
Nanyang Technological University
Email: ssundaram@ntu.edu.sg

## Slide 2: Representation
Bit – 1 or ‘0’
8 bits – byte
Word, long word representation is depends on the computer architecture
In general
  16 bits – word
  32 bits – long word
Why hexadecimal representation?
Notes: 3x12=36 2x12=24 1x12=12 … what 0x12 = 18

## Slide 3: Hand counting of Hexadecimal.

## Slide 4: Memory data formats

## Slide 5: Power Representation
2x | Value in Hexadecimal
20 | 1
21 | 2
22 | 4
23 | 8
24 | 10
25 | 20
26 | 40
27 | 80
28 | 100
29 | 200
2A () | 400
2B () | 800
2C () | 1000
2D () | 2000
2E () | 4000
2F () | 8000
210 () | 10000

## Slide 6: HS8/2000 Register

## Slide 7: Register…
8 32-bit register (ER0 to ER7)
It can be divided 16 (E0 to E7 and R0 to R7) 16-bit register
Extended register can be further divided into 16 8-bit register as RH0-RH7 and RL0-RL7.
ER7 – function as a stack pointer
General register division

## Slide 8: Control Register
Program Counter
  This 24-bit counter indicates the address of the next instruction the CPU will execute.
  The length of all CPU instructions is 16 bits (one word) or a multiple of 16 bits, so the least significant PC bit is ignored.
  When an instruction is fetched, the least significant PC bit is regarded as 0.
Condition-Code Register
  This 8-bit register contains internal CPU status information, including an interrupt mask bit (I) and half-carry (H), user bit (U), negative (N), zero (Z), overflow (V), and carry (C) flags.
Extended Control Register
  This 8-bit register contains the trace bit (T) and three interrupt mask bits (I2 to I0).
Bit 7—Trace Bit (T):
  When this bit is cleared to 0, instructions are executed in sequence.
  When this bit is set to 1, a trace exception is generated each time an instruction is executed.
Bit 6 to 3: Reserved (always read as 1)
Bits 2 to 0—Interrupt Mask Bits